## Slide 1: Power in the Field
Curtis V. Macchioni
Nightfall, November 5, 2021

## Slide 2: My Background
  Physicist with 38 years in technology development
  1st telescope: 2.4” Unitron Refractor
  Currently use C11 Edge on SB MX & MyT
  2008 – 2018 Camera Assisted Viewing, or EAA
  2019 – Now Beginner Astrophotographer

## Slide 3: My Quest for Better Power
  10+ Yrs: Power from lead acid batteries/ gas generator
  2020 -2021 Comprehensive Analysis of Lithium Batteries
    General review of Li battery technology
    Talked with multiple vendors/manufacturers
    Checked battery reviews, ratings, specs
    Toured Battleborn’s Reno, NV factory
    Conducted extensive real world use tests of multiple batteries
Jackery 1002Wh Solar
Generator &
Solar Panels
Battleborn
100 Ah LiFePO4 Battery

## Slide 4: Why Lithium?
Feature | Lithium 100Ah Battery | AGM 100Ah Battery
Lifetime | 10 years | 4-5 years
# Discharge Cycles | >2500 | 450 to 550
Depth of Discharge Without Damage | 100% | 50 – 70%
Weight | 31 lbs | 63 lbs
Flat Voltage Curve | Yes | No
Battery Management System (BMS) | Yes | No
Charge Rate / Charge Time | 0.5C / T | 0.3C / 1.7T
Memory effect | No | Yes
Self-discharge Rate | 2-3% / Month | 4 – 6% / Month
Maintenance | 6 months | Monthly
Cost | $400 to $800 | $169 to $290
Upfront Cost Per Watt-Hour | $0.31 to $0.62 | $0.26 to $0.45
Lifetime Cost per KiloWatt-Hour | $0.12 to $0.25 | $0.48 to $0.82

## Slide 5: Many Lithium Battery Chemistries
Lithium Cobalt Oxide, LiCoO2 (ICR)
Lithium Nickel Manganese Cobalt Oxide, LiNiMnCoO2 (NMC)
Lithium Manganese Oxide, LiMn2O4 (LMO)
Lithium Nickle Cobalt Aluminum Oxide, LiNiCoAlO2 (NCA)
Lithium Iron Phosphate, LiFePO4 (LFP)
Lithium Titanate, Li2TiO3 (LTO)
We will focus the two most relevant to us
  LiFePO4 - found in most stand alone Lithium batteries
  LiNiMnCoO2 - found in most solar generators

## Slide 6: Key Characteristics of LFP & NMC
LiFePO4 (LFP)
  Very high cycle life >2500 cycles
  Very high thermal runaway temperatures 518o F
  Nominal cell voltage 3.2 to 3.3V –> 4 x 3.2 = 12.8V
  Low specific energy density 90 -120Wh/kg
  Primarily used for RVs, Boats
LiNiMnCoO2 (NMC)
  Very high specific energy densities 150 – 220Wh/kg
  High thermal runaway temperature 410o F
  Moderate cycle life >500 cycles
  Nominal cell voltage 3.6 to 3.7V -> 4 x 3.6 = 14.4V
  Primarily used for power tools, E-Bikes, Electric Cars, Solar Generators

## Slide 7
Polymer Pouch Cells
  Foil pouch, thin profile, highest packing efficiency
  Phones, Laptops, Tablets, Chevy Volt
Prismatic Cells
  Strong welded case, difficult to manufacture consistently
  High packing efficiency but poor thermal management
  Large capacity per cell requires fewer cells
  Harder to balance cells, single cell failure catastrophic
  Phones, Laptops, Tablets
Cylindrical Cells
  Cheapest to manufacture, automated/consistent process
  Lower packing efficiency but good thermal management
  Easy to balance cells, single cell failure has minimal impact
  Power tools, E-Bikes, Medical, Tesla
3 Basic Lithium Cell Package Types

## Slide 8: Inside a Lithium Battery: Li Cells
Cylindrical Cells are the most common: Arranged in series/parallel configuration to obtain the V & Amp-Hr
  Battleborn 100Ah: 120 Cylindrical Cells
  4 (series) x 30 (parallel) =120 cells
  4 x 3.2V / cell = 12.8V 30 x 3.4Ah / cell = 102Ah
Prismatic Cells are less common: Fewer cells arranged in series
  AmpereTime 50Ah: 4 Prismatic Cells
  4 (series) X 3.2V / cell = 12.8V
  1 x 50Ah / cell = 50 Ah

## Slide 9: Tesla Battery Cells
Image from https://www.easyelectriccars.com

## Slide 10: BMS, a Key Difference with Lead Acid
Lithium batteries have a battery management system (BMS) inside (if not don’t buy it)
  Function is to manage & protect the battery from unsafe operation:
    Low temp charging (25 to 32 deg F) & high temp (135 deg F) discharging or discharging
    Short disconnect
    Overcharging / over discharging
    Cell balancing
    Low voltage disconnect – key to allowing 100% DOD without damaging internal cells
  Not all BMSs are equal: check out Will Prowse’s tear down videos
    Aliexpress 120Ah LiFePO4 Battery https://www.youtube.com/watch?v=OW3QCeWFDys
    Battleborn https://www.youtube.com/watch?v=G5E30u-66VI

## Slide 11: A Plethora of LiFePO4 Battery Choices
Dozens of different options available with a few examples shown in the table below
  Most made and sold through China on Amazon or their manufacturer’s own web site
  Bioenno Power (Santa Ana, CA): Uses a Chinese contract manufacturer
  Battleborn (Sparks, NV.): Designed & assembled in the U.S. with cells from Asia
  Lowest cost is not always the best choice, there are trade-offs. Do your homework
Supplier | Wh | Ah | Max.12V Current | Weight (lbs) | Additional Features | Cost
Talentcell Cylindrical | 83.2 | 6.5 | 5A | 1.7 | 1 x 5.5 x 2.1, USB | $53
Celestron | 159 | 12.4 | 10 A & 5A | 4.5 | 10A Car, 5A 5.5 x 2.1, 2 x USB | $199
Bioenno Pwr Cylindrical | 640 | 50 | 50 | 13.3 | Anderson Power Pole Connectors | $470
Expert Power Prismatic | 1280 640 | 100 50 | 100A 50A | 22.6 13 | Standard high capacity battery terminals | $640 $450
Battleborn Cylindrical | 1280 640 | 100 50 | 100A 50A | 31 17.6 | Standard high capacity battery terminals | $800 $500
AmpereTime Prismatic | 1280 640 | 100 50 | 100A 50A | 25.5 11.6 | Standard high capacity battery terminals | $400 $200
Images – Amazon.com, Battelbornbatteries.com, Bioennopower.com, Celestron.com

## Slide 12: Solar Generators
Solar Generators have many useful built-in features not available on a stand alone battery
  Built-in DC power port(s): Voltage regulated 10A DC cigarette socket; May have additional ports
  Pure Sine Wave inverter for AC power with 1 or more ports
  Built in charge controller for solar panel charging
  Multiple USB charging ports,
  Display showing the Power and SOC
  BMS to protect and manage the battery cells
  AC wall charger included
Maxoak Bluetti AC50s 500Wh
Jackery 518Wh

## Slide 13: Inside a Lithium Solar Generator
Jackery Explorer 1000
  AC Inverter, Solar Charge Controller
  BMS, Input/Output connections
  Display and meter
  6 (series) x 16 (parallel) = 96 total cells
  6 x 3.6V = 21.6V, hence the voltage regulator  nominal output ~12.8V
  16 x 2.9Ah = 46.4Ah @ 21.6V  83.5Ah @ 12V
  Link to teardown video https://www.youtube.com/watch?v=AKxt4eAwKRU
AC Inverter
Li Battery Cells

## Slide 14: A Plethora of Solar Generators
Dozens of different options available with a few examples shown in the table below
  Most made and sold through China on Amazon or their manufacturer’s own web site
  Jackery & Goal Zero are probably the most well known brands
Supplier | Wh | Ah | Weight (lbs) | Additional Features | Cost
Meade NMC | 222 | 18.5 | 6.3 | 2 AC Ports (100W), 5 x USB 3x 10A 5.5 x 2.1 (10A Total), 2 USB A, 2 USB C | $249
Maxoak Bluetti AC50S NMC Cyl. | 500 | 42 | 13.6 | 10A Regulated Cigarette Port, 2 x 5.5 x 2.1mm 3A Ports, 1 AC Port (300W), 4 x USB A, 45W PD Port, Display, Power Meter | $380
Jackery 500 NMC Cyl. | 518 | 43 | 13.3 | 10A Regulated Cigarette Port, 2x 3A Regulated DC Ports, 1 AC Port (500W), 3 USBA, Display, Pwr Meter | $425
Jackery 1000 NMC Cyl. | 1002 | 83 | 22 | 10A Regulated Cigarette Port, 3 AC Ports (1000W), 2 USBA, 2 USBC, Display, Power Meter | $850
Golabs R300 LiFePO4 Cyl. | 299 | 25 | 10.5 | 10A Unregulated Cigarette Port, 2 x 5.5 x 2.1mm Ports (10A Max)2 AC Ports (300W), 2 USB QC,1 PD 30W, 1 PD 60W Display, Power Meter | $200
Goal Zero Yeti 505Wh NMC Cyl. | 500 | 42 | 12.9 | 10A Regulated Cigarette Port, 6mm DC Port, 2 x AC (300W), 2 x USB A, 1 USB C, 1 USB C PD, Display, Power Meter | $699
Images – Amazon.com, Battelbornbatteries.com, Bioennopower.com, Celestron.com

## Slide 15: Li Battery vs Li Solar Generator
Feature | Lithium 100Ah Battery | Solar Generator 1002WH
Capacity | 100Ah (1280Wh) | 78Ah (1002Wh)
Lifetime | 10 years | 10 years
# Discharge Cycles | >2500 | >500
Depth of Discharge Without Damage | 100% | 100%
Weight (Normalized to 100Ah) | 31 lbs (31 lbs) | 22 lbs ( 28 lbs)
Voltage Regulation | No | Yes
Battery Management System (BMS) | Yes | Yes
Cigarette Lighter Port | No | Yes
Pure Sine Wave Inverter | No | Yes
USB Ports | No | Yes
Solar Charge Controller | No | Yes
Display & Power Meter | No | Yes
Cost per WH | $0.31 to $0.62 | $0.94
Lifetime Cost per KiloWatt-Hour | $0.12 to $0.25 | $1.70 to $2.00

## Slide 16: Test Results for 5 Li Power Supplies
Capacity Test
Voltage Discharge Curve Test
Run Time in the Field Test
Battleborn 100Ah & Bioenno Power 50Ah LiFePO4 batteries
Jackery Explorer 1000 and 500
Maxoak Bluetti AC50S 500

## Slide 17: 1st Test: Actual vs Rated Capacities
Capacities shown are for V > 12.0V
Average of multiple measurements for each
Battleborn manufactures their batteries to between 104 and 108% of spec
Results for Jackery and Bluetti solar generators are consistent with other reviews
Power Source | Rated Ah | Actual Ah | Rated Wh | Actual Wh
Battleborn 100Ah | 100 | 105 (105%) | 1280 | 1356 (106%)
Bioenno 50Ah | 50 | 45 (90%) | 640 | 575 (90%)
Jackery 1000 | 78.6 | 70 (90%) | 1002 | 908 (91%)
Jackery 500 | 40.6 | 42.5 (105%) | 518 | 549 (106%)
Bluetti 500 | 39.2 | 35.4 (90%) | 500 | 465 (93%)

## Slide 18: 2nd Test: Voltage Discharge vs DOC
Solar Generator maintained a constant voltage of 12.75V at 60W until shut-off
LiFePO4 batteries drop from 12.9V at 60W to 11.9V after 96% DOD
Lead Acid voltage drops to 12.06V at 50% DOD, below 12.0V at ~58% DOD

## Slide 19: 3rd Test: Field Test Setups
  Multiple nights in the field for each Li supply
DC:
    Celestron C11 on Software Bisque MyT mount
      ASI1600MC uncooled camera
      ASI240MC camera
      ASI guide cameras
    Beelink Mini-PC running TSX
    Astrozap 11” dew strap
    Celestron motor focuser; Temp-est Cooling Fans
    Pegaus Power Box Advanced Power/USB Hub
    Gl.iNet Wireless Router
  AC:
    Dell 15” XPS laptop running TSX
    MyT mount powered with its AC supply
      ASI240MC TEC, ASI guide camera & Celestron focuser

## Slide 20: Actual Power Requirements
  Measurements made with a Pegasus Power Box Advanced averaged over ~ 20min each
  Software Bisque specs TheSky Fusion at 4 – 8W; Raspberry Pi4 should be ~ 4-5W
  Mount power will vary with load, balance and orientation
  Currents are shown at 13V, the nominal voltage of my Pyramid regulated power supply

## Slide 21: Dark Site Run Time Summary
Power supply size required depends upon # run time hrs per night and # nights before a re-charge is possible
Any of the above supplies will run a 60W load for at least 1 full night
Equipment Setup | Expected Run Times | Expected Run Times |  | Rated Wh |  | 
Equipment Setup | Power Needed | Battleborn 100Ah | Bioenno 50Ah | Jackery 1000 | Jackery 500 | Bluetti 500
Rasberry Pi, NUC or Mini-PC, Tracking Mount, Uncooled Camera, Guider, Focuser, Filter Wheel, Powered Hub | 20 – 30W | 67.8 to 45 hrs | 28.8 to 19 hrs | 45.4 to 30.3 hrs | 27.5 to 18.3 hrs | 23.3 to 15.5 hrs
Above + Dew Heater and/or Camera Cooling | 30 – 60W | 45 to 22.6 hrs | 19 to 9.5 hrs | 30.3 to 15.1 hrs | 18.3 to 9.1 hrs | 15.5 to 7.8 hrs
Above + 15.4" Laptop in place of Mini-PC | 60 – 120W | 22.6 to 11 hrs | 9.5 to 4.5 hrs | 15.1 to 7.6 hrs | 9.1 to 4.6 hrs | 7.8 to 3.9 hrs

## Slide 22: Charging Lithium Power Supplies
Cannot be charged below 25 to 32 deg F nor above 131 deg F (depends on model)
AC
  Solar generators come with an AC charger
  Batteries require a lithium capable charger – different charge profile from lead acid
Solar
  Solar generators only need a solar panel with compatible connector
  Batteries require a lithium capable charge controller, a solar panel and compatible connectors

## Slide 23: Full Charge Cycle Times
Solar generator re-charge times are limited by their charging circuit current maximum
Equipment Setup | 0% SOC to 100% SOC Charging Times (hrs) |  | Rated Wh |  | 
Equipment Setup | Battleborn 100Ah | Bioenno 50Ah | Jackery 1000 | Jackery 500 | Bluetti 500
Included Charger | N/A | N/A | 6.5 to 7 | 6.5 to 7 | 7 to 7.5
20A Lithium Charger | 5-6 | 2.5 | N/A | N/A | N/A
100W Solar Panel | 20 | 8 | 10.5 | 9.5 | 6 to 6.5
2 x 100W Solar Panel | 10 | 4 | 8 |  | 

## Slide 24: Wrap Up
  Lead acid batteries work, are cheap and will continue to be the choice of many
  Lithium batteries with their many advantages are gaining traction fast
  Solar Generators are more expensive than simple Li battery, but provide significantly more features

## Slide 25: References
  You can find the following information on my web site https://www.californiaskys.com/
    This presentation which you may use yourself so long as you provide attribution
    Reviews of the Jackery Explorer 1000, Jackery 500, Bluetti AC50S and Bioenno Power 50Ah LiFePO4 battery. A review of the Battleborn 100Ah battery is coming soon.
    A review of the Jackery Solar Saga 100W Solar Panels
    Links to all of the power supplies discussed today, along with links to useful cables and adapters